## Slide 1: Poise: Balancing Thread-Level Parallelism and Memory System Performance in GPUs using Machine Learning
HPCA 2019
Washington D.C., USA
19th February, 2019
Saumay Dublish* Vijay Nagarajan ‡ Nigel Topham‡
* Synopsys Inc.
‡ The University of Edinburgh

## Slide 2
GPU Architecture
Overview
GPUs are throughput-oriented systems
Focus on overall system throughput
Rely on high levels of multithreading
Implemented by switching across warps
Overlap latency with useful execution
DRAM
SM
SM
SM
L2
L1
L1
L1
Overview
GPU Architecture
Notes: GPUs are throughput oriented systems that are concerned with overall system performance and not with single threaded performance.
To achieve this goal, they allow concurrent execution of thousands of threads and use multithreading to maximize system performance.

## Slide 3
GPU Architecture
Consequence of increasing TLP
Increasing TLP not always useful
Leads to cache thrashing
Leads to bandwidth bottlenecks
Results in high levels of congestion
Latencies tend to be very high!
Can such high latencies be hidden?
DRAM
SM
SM
SM
L2
L1
L1
L1
Consequence of increasing TLP
GPU Architecture
Notes: Increasing TLP is not always useful

## Slide 4
Instruction concurrency
Warp concurrency
(Intra-warp concurrency)
LOAD
Independent
Independent
Independent
Independent
DEPENDENCY
Harnessing concurrency
time
Hiding Latencies in GPUs
(Inter-warp concurrency)
LOAD
Independent
Independent
Independent
Independent
DEPENDENCY
LOAD
Independent
Independent
Independent
Independent
DEPENDENCY
LOAD
Independent
Independent
Independent
Independent
DEPENDENCY
LOAD
Independent
Independent
Independent
Independent
DEPENDENCY
LOAD
Independent
Independent
Independent
Independent
DEPENDENCY
time
Load latency
Execution
Load latency
Execution
Hiding Latencies in GPUs
GPU Architecture
Notes: A warp typically hosts a load instruction and an instruction dependent on the load with a bunch of independent operations in between

## Slide 5
Instruction concurrency
Warp concurrency
LOAD
Independent
Independent
Independent
Independent
DEPENDENCY
time
stall
Hiding Latencies in GPUs
(Intra-warp concurrency)
(Inter-warp concurrency)
Harnessing concurrency
LOAD
Independent
Independent
Independent
Independent
DEPENDENCY
LOAD
Independent
Independent
Independent
Independent
DEPENDENCY
LOAD
Independent
Independent
Independent
Independent
DEPENDENCY
LOAD
Independent
Independent
Independent
Independent
DEPENDENCY
LOAD
Independent
Independent
Independent
Independent
DEPENDENCY
time
Load latency
Execution
Load latency
Execution
Hiding Latencies in GPUs
GPU Architecture
Notes: But a single warp does not provide enough concurrency to hide the entire memory latency

## Slide 6
Instruction concurrency
Warp concurrency
LOAD
Independent
Independent
Independent
Independent
DEPENDENCY
time
stall
LOAD
Independent
Independent
Independent
Independent
DEPENDENCY
LOAD
Independent
Independent
Independent
Independent
DEPENDENCY
LOAD
Independent
Independent
Independent
Independent
DEPENDENCY
LOAD
Independent
Independent
Independent
Independent
DEPENDENCY
LOAD
Independent
Independent
Independent
Independent
DEPENDENCY
time
Hiding Latencies in GPUs
(Intra-warp concurrency)
(Inter-warp concurrency)
Harnessing concurrency
Works well in compute-intensive applications
Load latency
Execution
Load latency
Execution
Hiding Latencies in GPUs
GPU Architecture
Notes: Load latencies get overlapped due to memory level parallelism, and busy cycles get added.
Instruction concurrency - Independent instructions within a warp
Warp concurrency - Independent instructions interleaved across warps

## Slide 7
LOAD
Independent
Independent
Independent
Independent
DEPENDENCY
LOAD
Independent
Independent
Independent
Independent
DEPENDENCY
LOAD
Independent
Independent
Independent
Independent
DEPENDENCY
LOAD
Independent
Independent
Independent
Independent
DEPENDENCY
Instruction concurrency
Warp concurrency
LOAD
Independent
Independent
Independent
Independent
DEPENDENCY
time
Fewer independent operations
LOAD
Independent
Independent
Independent
Independent
DEPENDENCY
time
stall
(Intra-warp concurrency)
(Inter-warp concurrency)
The Case of Limited Parallelism
Load latency
Execution
Load latency
Execution
The Case of Limited Parallelism
GPU Architecture
Notes: But there are a growing set of applications with very few independent operations in a warp

## Slide 8
Instruction concurrency
Warp concurrency
time
time
stall
stall
LOAD
Independent
Independent
Independent
Independent
DEPENDENCY
LOAD
Independent
Independent
Independent
Independent
DEPENDENCY
LOAD
Independent
Independent
Independent
Independent
DEPENDENCY
LOAD
Independent
Independent
Independent
Independent
DEPENDENCY
LOAD
Independent
Independent
Independent
Independent
DEPENDENCY
LOAD
Independent
Independent
Independent
Independent
DEPENDENCY
(Intra-warp concurrency)
(Inter-warp concurrency)
Fewer independent operations
The Case of Limited Parallelism
Load latency
Execution
Load latency
Execution
The Case of Limited Parallelism
GPU Architecture

## Slide 9
Instruction concurrency
Warp concurrency
time
time
Load latency
Execution
stall
Impractically large number of warps required to completely hide latency
Higher load latency due to congestion
LOAD
Independent
Independent
Independent
Independent
DEPENDENCY
LOAD
Independent
Independent
Independent
Independent
DEPENDENCY
LOAD
Independent
Independent
Independent
Independent
DEPENDENCY
LOAD
Independent
Independent
Independent
Independent
DEPENDENCY
LOAD
Independent
Independent
Independent
Independent
DEPENDENCY
LOAD
Independent
Independent
Independent
Independent
DEPENDENCY
LOAD
Independent
Independent
Independent
Independent
DEPENDENCY
LOAD
Independent
Independent
Independent
Independent
DEPENDENCY
LOAD
Independent
Independent
Independent
Independent
DEPENDENCY
LOAD
Independent
Independent
Independent
Independent
DEPENDENCY
LOAD
Independent
Independent
Independent
Independent
DEPENDENCY
LOAD
Independent
Independent
Independent
Independent
DEPENDENCY
LOAD
Independent
Independent
Independent
Independent
DEPENDENCY
LOAD
Independent
Independent
Independent
Independent
DEPENDENCY
LOAD
Independent
Independent
Independent
Independent
DEPENDENCY
LOAD
Independent
Independent
Independent
Independent
DEPENDENCY
(Intra-warp concurrency)
(Inter-warp concurrency)
Fewer independent operations
The Case of Limited Parallelism
Load latency
Execution
The Case of Limited Parallelism
GPU Architecture
Notes: In order to have the same level of parallelism that we had in compute-intensive applications, one would need impractically large number of warps.
It is often not possible to have so many warps due to resource constraints and hardware limitations.
Within practical limits, it only increases the memory latency without significantly improving the parallelism

## Slide 10
Need For Balance
Tension between TLP and memory system performance
  Increase TLP to improve concurrency – latency worsens
  Reduce TLP to reduce latency – concurrency worsens
Memory Performance
Concurrency
☓
✓
☓
✓
Optimal system throughput with balanced TLP and memory performance
Need for Balance
GPU Architecture
Notes: Case 1: Lower system throughput due to high congestion and exposed latencies
Case 2: Lower system throughput due to restricted parallelism
Somewhere in the middle lies a balance which provides sufficient concurrency without causing cache thrashing and memory congestion

## Slide 11
Outline
Problem Statement Balancing TLP and memory performance
Prior state-of-the-art CCWS and PCAL warp schedulers
Pitfalls in prior techniques Iterative search and prone to local optima
Goals Computing the best warp scheduling decisions
Proposal Poise
Results Experimental results
Conclusion Key takeaways

## Slide 12
Prior state-of-the-art
L1 cache
Warps
Cache-conscious wavefront scheduling (CCWS)
  Limits the degree of multithreading
Cache Thrashing
Memory Congestion
CCWS
Prior state-of-the-art
Notes: One of the first few techniques to propose reducing TLP to improve system throughput was CCWS.
The authors recognized that high number of warps cause cache thrashing and congestion, and suggested reducing these warps

## Slide 13
Prior state-of-the-art
L1 cache
Warps
Reduces cache thrashing
Relieves congestion
☓
Cache-conscious wavefront scheduling (CCWS)
Cache Thrashing
Memory Congestion
Shortcomings
Couples warps with cache performance
Underutilization of shared memory resources
Dynamic policy has significant performance and cost overheads
Static policy burdens the user with the task of profiling every workload
CCWS
Prior state-of-the-art
  Limits the degree of multithreading

## Slide 14
☓
☓
Prior state-of-the-art
L1 cache
Warps
CCWS
Prior state-of-the-art
Priority-based cache allocation (PCAL)
Alter parallelism independent of memory system performance
Notes: PCAL continues to use lower number of warps to maintain good cache performance

## Slide 15
Prior state-of-the-art
L1 cache
Warps
☓
Priority-based cache allocation (PCAL)
Vital warps (W1, W2, W3)
Cache-polluting warps
(W1, W2)
Cache-polluting warps
Vital warps
PCAL search space
CCWS search space
PCAL
Prior state-of-the-art

## Slide 16
Prior state-of-the-art
Priority-based cache allocation (PCAL)
Vital warps (N)
Determine degree of multithreading
Cache-polluting warps (p)
Subset of vital warps
Ability to allocate and evict the L1 cache
Reduce cache contention
Warp-tuple { N, p }
Cache-polluting warps
Vital warps
PCAL search space
CCWS search space
PCAL
Prior state-of-the-art
Notes: High TLP maybe counter-productive as it increases the latencies which we wanted to hide in the first place
Instruction concurrency - Independent instructions within a warp
Warp concurrency - Independent instructions interleaved across warps

## Slide 17
Limitations of PCAL
Heuristic-based iterative search are slow in hardware
Prone to local optima in presence of multiple performance peaks
These two limitations lead to sub-optimal solutions
Cache-polluting warps
Vital warps
Iterative hill climbing
Local optimum
Limitations of PCAL
Prior state-of-the-art
Notes: Heuristics based iterative search are particularly slow in hardware due to the time needed to generate the heuristics which is typically by sampling.
The impact is even more when the starting point is far from the solution.
Iterative searches can get trapped in a local optima when there are multiple performance peaks in the search space, which is in fact true for GPUs.

## Slide 18
Cache-polluting warps
Vital warps
Balance TLP and memory performance
Avoid local optima
Converge expeditiously
Low sampling and hardware overhead
Avoid burdening the user
Goals
Best warp-tuple?
How to find the best warp-tuple?
Goals
Notes: While we have described the problem before – striking a balance between TLP and memory system performance
We now define the problem statement further – through the levers defined by PCAL – how to find the best warp-tuple that best balances TLP and memory
Challenges:
Heuristics based iterative search are prone to local optima in presence of multiple performance peaks in the solution space
Iterative search is slow in hardware
It should not add profiling burden on the user like several profiling based techniques do

## Slide 19
A technique to dynamically balance TLP and memory system performance
Proposal
Poise
Machine Learning Framework
Hardware Inference Engine
Training Dataset
Feature Set
Sample Input
Sample Output
Best warp-tuple
Regression Model
Supervised learning
Feature weights
Prediction Stage &
Local Search
Runtime prediction
Runtime Input
Unseen user application
Poise Prediction
Best warp-tuple
via compiler
Profiled Kernels
Poise: A System Overview
Poise
Notes: The machine learning framework comprises a training set which is used to learn about good warp scheduling decisions
The profiled kernels feed sample input and output to the regression model which performs supervised learning
It learns a mapping from input to output and conveys that learning to the hardware throught the compiler

## Slide 20
Black-box techniques provide little insight
Analytical model uses domain knowledge to identify reliable features
Allows us to reason about the effectiveness of different features
Proposed feature vector consists of only seven features
More details about the analytical model in the paper
Machine Learning Framework
Analytical Model
Analytical Model
Machine Learning Framework
Poise
Notes: Often times, correlation techniques and other black box techniques are used to find the feature set. But they provide little insight as to why certain features are selected.
This limits their adoption is rigid systems such as architectures where one must burn the logic into the chip and does not allow changes so easily.

## Slide 21
We use Negative Binomial regression to perform supervised learning
Inputs are mapped to the output using a log-linear link function
Reasons for selecting Negative Binomial regression:
  Predicts discrete non-negative warp-tuple values
  Lightweight in training time and dataset
  Low computational demand for training and inference
Machine Learning Framework
Regression Model
Regression Model
Machine Learning Framework
Poise
Notes: Larger models: overfitting; bulky features; black box
Larger models are prone to overfitting when the training datasets are not huge and present large requirements on training data and time
Generate bulky feature weight matrices which often run into Kilo Bytes and Mega Bytes and cannot be stored on-chip due to storage constraints,
Are black box techniques that prevents us to reason about the efficiency of these techniques and hinders adoption in architecture

## Slide 22
Computes runtime predictions about good warp-tuples for new workloads
Constitutes a prediction stage and local search
Hardware Inference Engine
Training Dataset
Feature Set
Sample Input
Sample Output
Best warp-tuple
Regression Model
Feature weights
Prediction Stage & Local Search
Runtime Input
Unseen user application
Poise prediction
Best warp-tuple
via compiler
Hardware Inference Engine
Poise

## Slide 23
Hardware Inference Engine
Prediction Stage
Perform predictions at runtime using new features and learned mapping
Feature weights
Prediction Stage
Runtime Input
Unseen user application
Predicted Output
Good warp-tuple
via compiler
Dot product
Weights ● Features
Inference
Inverse log operation
Runtime Feature Collection
Performance Counters
Prediction Stage
Hardware Inference Engine
Poise

## Slide 24
Hardware Inference Engine
Local Search
Mitigate statistical errors in prediction with a near-neighborhood search via gradient ascent
Feature weights
Prediction Stage
Runtime Input
Unseen user application
Predicted Output
Good warp-tuple
via compiler
Local Search
Poise Prediction
Best warp-tuple
Warp Scheduler
Local search is less prone to getting trapped at local optima due to proximity to performance peaks
Local Search
Hardware Inference Engine
Poise
Notes: It’s worth noting, that unlike PCAL, local search here is less prone …

## Slide 25
Working Summary
Cache-polluting warps
Vital warps
Cache-polluting warps
Vital warps
Poise
PCAL
Iterative hill climbing
Local optimum
Feature collection
Feature collection
Prediction
Local Search
Working Summary
Poise

## Slide 26
Warp Scheduler Architecture
WMAX-1
…
…
…
…
W2
W1
W0
Warp Scheduler Queue
Warp-ID
bits
Oldest
Latest
GTO warp scheduler
Warp Scheduler Architecture
Poise

## Slide 27
Warp Scheduler Architecture
WMAX-1
…
…
…
…
W2
W1
W0
Warp Scheduler Queue
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
Warp-ID
bits
Vital bit
Pollute bit
Oldest
Latest
Warp Scheduler Architecture
Poise

## Slide 28
Warp Scheduler Architecture
WMAX-1
…
…
…
…
W2
W1
W0
Warp Scheduler Queue
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
Warp-ID
bits
Vital bit
Pollute bit
Oldest
Latest
WMAX-1
…
…
…
…
W2
W1
W0
0
0
1
1
1
1
1
1
N
Vital Warps
Constant
Memory
Hardware Inference Engine
Compiler
Vital warps (N)
Cache-polluting warps (p)
Feature weights
Warp Scheduler Architecture
Poise
Notes: At runtime, the compiler provides the 8 features weights for 7 features and 1 intercept to the constant memory
The HIE uses those weights and collected features to compute the link function, performs local search and generates a prediction for the warp tuple

## Slide 29
Warp Scheduler Architecture
Constant
Memory
Hardware Inference Engine
Compiler
Vital warps (N)
Cache-polluting warps (p)
WMAX-1
…
…
…
…
W2
W1
W0
Warp Scheduler Queue
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
Warp-ID
bits
Vital bit
Pollute bit
Oldest
Latest
WMAX-1
…
…
…
…
W2
W1
W0
0
0
1
1
1
1
1
1
p
Cache-polluting
warps
0
0
0
0
0
1
1
1
Feature weights
Warp Scheduler Architecture
Poise

## Slide 30
Warp Scheduler Architecture
Constant
Memory
Hardware Inference Engine
Compiler
Vital warps (N)
Cache-polluting warps (p)
WMAX-1
…
…
…
…
W2
W1
W0
Warp Scheduler Queue
0
0
1
1
1
1
1
1
0
0
0
0
0
1
1
1
Warp-ID
bits
Vital bit
Pollute bit
Oldest
Latest
L1 Cache
Feature weights
Warp Scheduler Architecture
Poise
}
LOAD [a]
(bypass on read miss)
Do not pollute cache
}
LOAD [b]
Allocate and replace cache lines
}
Do not participate in TLP
Notes: ….
….
Through this mechanism, the system sustains good TLP while also maintaining good cache performance and mitigating bandwidth bottlenecks.

## Slide 31
Evaluation
Platform
  Statsmodels – regression analysis
  GPGPU-Sim (v3.2.2) – cycle-accurate simulator
  GPUWattch (McPAT) – energy and area estimation
Benchmark Suites *
  Rodinia
  MapReduce
  Graph Suite
  Polybench
*Training and evaluation are done on disjoint set of benchmarks
Methodology
Evaluation

## Slide 32
Evaluation
Baseline GPU configuration
  32 Streaming Multiprocessors (SM)
  16 KB Private L1 Cache
  2.25 MB Shared L2 Cache
  GTO warp scheduler
  48 warps per SM
Methodology
Evaluation

## Slide 33
Evaluation
Warp Scheduling Schemes
  GTO
    Baseline greedy-then-oldest warp scheduler
    Maximum warps enabled per SM for multithreading
  SWL
    Static Warp Limiting from the CCWS scheduler
    No runtime overheads in a static policy
  PCAL-SWL
    Dynamic PCAL policy with SWL for initial start
  Static-Best
    Each kernel run at best performing warp-tuple
    Determined by offline profiling of each kernel
Methodology
Evaluation

## Slide 34
Results
Performance
21.8%
31.5%
46.6%
52.8%
Poise outperforms PCAL-SWL by 15.1% on average
Results
Evaluation
Notes: Performance gap between Poise and Static-Best can be due to prediction errors or the local search overheads
Poise detects phase changes in monolithic kernels which go undetected in Static profiling

## Slide 35
Results
L1 Hit Rate
20.6%
37.7%
27.1%
40.1%
Poise reduces cache thrashing and reduces pressure on memory system
Results
Evaluation

## Slide 36
Results
Energy consumption
51.6%
79%
Poise reduces the energy consumption by 51.6% over GTO
Results
Evaluation

## Slide 37
Hardware Overhead
Arithmetic Units for link function computation
  Enough spare cycles in existing FP units
  Time-multiplexing existing FP units on SM
  No extra hardware needed
Feature collection
  Seven 32-bit hardware performance counters per SM
Finite State Machine
  Two 3-bit registers per SM
Modified Warp Scheduler
  2-bits per entry in warp scheduler queue
Net storage overhead of 40.75 bytes per SM
Hardware Overhead
Evaluation
Notes:   Required once in several hundreds of thousands of cycles
  Link function computation not in critical path

## Slide 38
Conclusion
Problem
  Investigate conflict between TLP and memory system performance
  Traditional techniques to balance are slow and sub-optimal
  Goal is to find good warp-tuples expeditiously in hardware
Proposal
  Poise – a machine learning based architectural technique
  Offline training to learn about good warp scheduling decisions
  Use prior knowledge to make good runtime predictions
Results
  Harmonic mean speedup of 46.6% over baseline GTO scheduler
  Extremely lightweight in terms of hardware overheads
  Demonstrate an effective use of ML to solve an architectural problem
Conclusion

## Slide 39
Questions?
Saumay Dublish
saumay.dublish@synopsys.com
http://homepages.inf.ed.ac.uk/s1433370/
Poise: Balancing Thread-Level Parallelism and Memory System Performance in GPUs using Machine Learning

## Slide 40
Backup Slides

## Slide 41
Discussion
Why not larger models such as DNNs?
  Bulky nature of complex models
  Generate prohibitively large feature weight matrices with high storage needs
  High computational demands for training and inference
  Black box nature of complex models and feature sets
  Lack of mathematical insights prevents reasoning
Discussion
Notes: Larger models: overfitting; bulky features; black box

## Slide 42
Discussion
Poise – a machine learning based architecture technique
  Harness domain knowledge to reduce model size and feature vector
  Small, yet effective regression model
  Inference has low computational and storage needs
  Viable architectural mechanism
  Demonstrate an effective use of ML to solve an architectural problem
Conclusion
Notes:   Allows future adaptability by allowing changes to feature weights through the compiler interface

## Slide 43
The Case of Limited Parallelism
Fewer independent operations per warp
Low instruction concurrency
Compensated by high warp concurrency
Pressure on memory system increases further
Latencies grow even more
May benefit from lower latencies – low TLP
Memory-sensitive applications
Notes: Load latencies get overlapped due to memory level parallelism, and busy cycles get added.
Instruction concurrency - Independent instructions within a warp
Warp concurrency - Independent instructions interleaved across warps

## Slide 44
Instruction concurrency
Warp concurrency
time
time
Load latency
Execution
stall
Improving memory-system performance is more useful
LOAD
Independent
Independent
Independent
Independent
DEPENDENCY
LOAD
Independent
Independent
Independent
Independent
DEPENDENCY
LOAD
Independent
Independent
Independent
Independent
DEPENDENCY
LOAD
Independent
Independent
Independent
Independent
DEPENDENCY
LOAD
Independent
Independent
Independent
Independent
DEPENDENCY
LOAD
Independent
Independent
Independent
Independent
DEPENDENCY
LOAD
Independent
Independent
Independent
Independent
DEPENDENCY
LOAD
Independent
Independent
Independent
Independent
DEPENDENCY
LOAD
Independent
Independent
Independent
Independent
DEPENDENCY
LOAD
Independent
Independent
Independent
Independent
DEPENDENCY
LOAD
Independent
Independent
Independent
Independent
DEPENDENCY
LOAD
Independent
Independent
Independent
Independent
DEPENDENCY
LOAD
Independent
Independent
Independent
Independent
DEPENDENCY
LOAD
Independent
Independent
Independent
Independent
DEPENDENCY
LOAD
Independent
Independent
Independent
Independent
DEPENDENCY
LOAD
Independent
Independent
Independent
Independent
DEPENDENCY
(Intra-warp concurrency)
(Inter-warp concurrency)
Fewer independent operations
The Case of Limited Parallelism
Load latency
Execution
The Case of Limited Parallelism
GPU Architecture
Higher load latency due to congestion

## Slide 45
Problem Statement
Balance TLP and memory system performance
Provide enough concurrency via TLP without significantly increasing memory latency

## Slide 46
Prior state-of-the-art
L1 cache
Warps
☓
Priority-based cache allocation (PCAL)
PCAL
Prior state-of-the-art
Alter parallelism independent of memory system performance
Notes: High TLP maybe counter-productive as it increases the latencies which we wanted to hide in the first place
Instruction concurrency - Independent instructions within a warp
Warp concurrency - Independent instructions interleaved across warps

## Slide 47
Results
Average Memory Latency
-10.7%
32.4%
1.1%
14.1%
Poise increases the AML by only 1.1% over GTO

## Slide 48
Results
Cache Bypassing & Stochastic Search
7.05%
24.2%
46.6%
Notes: APCM is a scheme to protect and bypass cache lines on the basis of instruction locality. It bypasses streaming accesses in the cache and protects high locality accesses.
Stochastic search uses a random starting point following by gradient ascent just like Poise.

## Slide 49
Training is done on a set of sample input-output pairs
Regression model learns a mapping from the input to the output
The learned mapping is expressed through feature weights
Feature weights are provided to the GPU via the compiler
Major components of the machine learning framework:
  Analytical Model
  Regression Model
Machine Learning Framework

## Slide 50
Working Summary
Cache-polluting warps
Vital warps
Cache-polluting warps
Vital warps
Poise
PCAL
Iterative hill climbing
Local optimum
Feature collection
Feature collection
Prediction
Local Search

## Slide 51
Instruction concurrency
Warp concurrency
(Intra-warp concurrency)
LOAD
Independent
Independent
Independent
Independent
DEPENDENCY
Harnessing concurrency
time
Load latency
Core Busy
Hiding Latencies in GPUs
(Inter-warp concurrency)
LOAD
Independent
Independent
Independent
Independent
DEPENDENCY
LOAD
Independent
Independent
Independent
Independent
DEPENDENCY
LOAD
Independent
Independent
Independent
Independent
DEPENDENCY
LOAD
Independent
Independent
Independent
Independent
DEPENDENCY
LOAD
Independent
Independent
Independent
Independent
DEPENDENCY
Notes: A warp typically hosts a load instruction and an instruction dependent on the load with a bunch of independent operations in between

## Slide 52
Hardware Inference Engine
Prediction Stage
Profiled Kernels
Analytical feature set
Sample Input
Sample Output
Best warp-tuple
Regression Model
Feature weights
Predictor
Runtime Input
Unseen user application
Predicted Output
Good warp-tuple
via compiler
Perform periodic predictions at runtime using feature weights and learned mapping
Prediction Stage
Hardware Inference Engine
Poise

## Slide 53
Results
Performance
21.8%
31.5%
46.6%
52.8%
Poise outperforms PCAL-SWL by 15.1% on average
Poise even surpasses Static-Best for monolithic kernels
Results
Evaluation
Notes: Performance gap between Poise and Static-Best can be due to prediction errors or the local search overheads
Poise detects phase changes in monolithic kernels which go undetected in Static profiling