## Slide 1: Evaluating and Mitigating Bandwidth Bottlenecks Across the Memory Hierarchy in GPUs
ISPASS 2017
25th April
Santa Rosa, California
Saumay Dublish, Vijay Nagarajan, Nigel Topham
The University of Edinburgh

## Slide 2
Multithreading on GPUs
Core
Core
Core
Core
DRAM
Kernel
Host CPU
to
GPU
Hardware
Scheduler
Cores hide memory latencies with concurrent execution

## Slide 3
Multithreading on GPUs
Core
Core
Core
Core
DRAM
Bandwidth Bottleneck
Kernel
Memory-intensive
applications
Host CPU
to
GPU
Hardware
Scheduler
Latencies grow
Appear in critical path

## Slide 4
Deeper Memory Hierarchy
Core
Core
Core
Core
DRAM
L2
L1
L1
L1
L1
Bandwidth filtering
Bandwidth filtering
High cache miss rates
Small caches
High multithreading
Distributed Bandwidth Bottleneck

## Slide 5
Deeper Memory Hierarchy
Core
Core
Core
Core
DRAM
L2
L1
L1
L1
L1
Bandwidth filtering
Bandwidth filtering
L2 roundtrip latency
̴ 300 cycles
(2-3x higher)
Distributed Bandwidth Bottleneck
High cache miss rates
Small caches
High multithreading

## Slide 6
Distributed Bandwidth Bottleneck
Deeper Memory Hierarchy
Core
Core
Core
Core
DRAM
L2
L1
L1
L1
L1
Bandwidth filtering
Bandwidth filtering
L2 roundtrip latency
̴ 300 cycles
(2-3x higher)
̴̴ 200 cycles
Identify and mitigate bottlenecks across the memory hierarchy
High cache miss rates
Small caches
High multithreading

## Slide 7
Goals
Characterize : Understand the bandwidth bottlenecks across different levels of the memory hierarchy such as L1, L2 and DRAM
Cause : Investigate the architectural causes for congestion
Effect : Design-space exploration to evaluate the effect of mitigating congestion
Proposal: Use cause and effect analysis to present cost-effective configurations of the memory hierarchy

## Slide 8
Experimental Environment
Platform
  GPGPU-Sim (v3.2.2)
  GPUWattch (McPAT)
Benchmark Suites
  Rodinia
  Parboil
  MapReduce

## Slide 9
Baseline Configuration
GTX 480 NVIDIA GPU
  15 SMs
  Private L1 Data Cache (16 KB; 32 MSHRs)
  Shared L2 Cache (768 KB; 32 MSHRs/bank)
  L1-L2 Interconnect (Crossbar; 32+32 bytes)
  DRAM (384 bits bus width)

## Slide 10
Latency Tolerance
Performance plateau
Latency tolerance
Performance versus Latency curve for memory-intensive benchmarks
Latency appears in the critical path

## Slide 11
Latency Tolerance
Performance plateau
[ 120 cycles ,
220 cycles ]
Ideal L2 access latency
Ideal DRAM access latency
Added latencies due to increasing congestion

## Slide 12
Performance plateau
  Baseline memory latencies critically higher than performance plateau latencies
  Baseline memory latencies critically higher than ideal access latencies to L2/DRAM
Observations about “baseline memory latencies”
[ 120 cycles ,
220 cycles ]
Ideal L2 access latency
Ideal DRAM access latency
Baseline Memory Latencies
Far from saturation
(theoretically possible)
Practically possible
to improve performance
Latency Tolerance
1x

## Slide 13
Infinite Bandwidth
2.37x

## Slide 14
Infinite Bandwidth
2.37x
1.15x
  Significant congestion in the cache hierarchy

## Slide 15
Understanding Bandwidth Bottleneck
  Decreasing bandwidth
  While the bandwidth provided decreases in the lower levels of the memory hierarchy, bandwidth demand does not reduce proportionally.
  This leads to a bandwidth skew between adjacent levels.
  As a result, requests queue up in the memory hierarchy for long durations, causing congestion.
  L2 access queues are full for 46% of its usage lifetime.
  DRAM access queue are full for 39% of its usage lifetime
Core
DRAM
L2
L1
L1 access
queue
L2 access
queue
DRAM
access queue

## Slide 16
Core
DRAM
L2
L1
  Structural Hazards
  Back Pressure
L1 MSHR
L2 MSHR
Causes of congestion

## Slide 17
Causes of congestion
Core
DRAM
L2
L1
  Prolonged contention for cache resources such as MSHRs or replaceable cache lines.
  Pending requests must complete and relinquish the resources.
  Therefore, new miss requests get serialized, increasing the memory latencies even more.
L1 MSHR
L2 MSHR
Structural Hazard
FULL
MISS
High cache hit latencies
HIT?
  Structural Hazards
  Back Pressure

## Slide 18
Core
DRAM
L2
L1
  Cascading effect of structural hazards
  Higher level gets throttled
  Eventually throttles core performance
L1 MSHR
L2 MSHR
X
X
STALL
Restricted parallelism on cores
Independent compute?
Causes of congestion
  Structural Hazards
  Back Pressure

## Slide 19
Core
DRAM
L2
L1
L1 cache stalls
L1 MSHR
L2 MSHR
11%
41%
  Structural Hazards
  Back Pressure
Causes of congestion

## Slide 20
  Back Pressure
Core
DRAM
L2
L1
L1 MSHR
L2 MSHR
48%
  L1 MSHR : 41% (Structural Hazards)
  L2 back pressure : 48% (Back pressure)
Major causes of stalls at L1
  Structural Hazards
L1 cache stalls
Causes of congestion

## Slide 21
L2 cache stalls
Core
DRAM
L2
L1
L1 MSHR
L2 MSHR
42%
  Crossbar (response path) : 42% (Back pressure)
  DRAM : 35% (Back pressure)
Major causes of stalls at L2
35%
  Back Pressure
  Structural Hazards
Causes of congestion

## Slide 22
Mitigating congestion
Core
DRAM
L2
L1
L1 MSHR
L2 MSHR
Category-1: Operate at peak throughput
  Minimize stalls by exploiting existing peak throughput
  e.g. MSHRs, Access Queue size
Category-2: Increase peak throughput
  Minimize stalls by increasing the peak throughput
  e.g. Crossbar flit size, DRAM bus width
Classifying the Design Space

## Slide 23
Identifying the Design Space
Core
DRAM
L2
L1
L1 MSHR
L2 MSHR
L1 parameters
  L1 Miss Queue
  L1 MSHR
  Memory pipeline width
L2 parameters
  L2 Miss/Response Queue
  L2 MSHR
  L2 Data Port Width
  L2 Banks
  Flit Size (Crossbar)
DRAM parameters
  Scheduler Queue
  Banks
  Bus width

## Slide 24
Mitigating congestion
Scaling L1 parameters by 4x
4%

## Slide 25
Scaling L1 parameters by 4x
4%
- 33%
- 25%
- 13%
- 7%
Improving bandwidth in isolation can lead to even more congestion at the lower levels
Mitigating congestion

## Slide 26
Improving bandwidth in isolation can lead to even more congestion at the lower levels
Core frequency scaling on real GTX 480
Mitigating congestion
Up to 23% slowdown

## Slide 27
Scaling L2 parameters by 4x
59%
Shows the criticality of the L2 bandwidth
Mitigating congestion

## Slide 28
Scaling DRAM parameters by 4x (HBM)
11%
Mitigating congestion

## Slide 29
Scaling L1 and L2 parameters by 4x
69%
59%
4%
- 13%
212%
226%
A case for synergistic scaling!
Mitigating congestion

## Slide 30
Scaling L1 and L2 parameters by 4x
69%
11%
Higher speedup on mitigating congestion in the cache hierarchy compared to DRAM (as done in HBM)
Mitigating congestion

## Slide 31
76%
Scaling L2 and DRAM parameters by 4x
Mitigating congestion

## Slide 32
90%
Scaling the entire memory hierarchy by 4x
Mitigating congestion

## Slide 33
Pruning the Design Space
Scaling all architectural parameters by 4x impractical
Need to prune the design space
We now know the …
  Causes of congestion (at each memory level)
  Effects of reducing congestion (at different memory levels)
Cost effective configuration
Mitigate causes where the effect is maximum
Boost bandwidth resources where it hurts most!

## Slide 34
Cost-effective Design Space
L1 parameters
  L1 Miss Queue
  L1 MSHR
  Memory pipeline width
L2 parameters
  L2 Miss/Response Queue
  L2 MSHR
  L2 Data Port Width
  L2 Banks
  Flit Size (Crossbar)
DRAM parameters
  Scheduler Queue
  Banks
  Bus width

## Slide 35
Cost-effective Design Space
L1 parameters
  L1 Miss Queue
  L1 MSHR
  Memory pipeline width
L2 parameters
  L2 Miss/Response Queue
  Flit Size (Crossbar)
Simple Buffers
Minimal cost of scaling
Scale by 4x

## Slide 36
Cost-effective design-space
L1 parameters
  L1 Miss Queue
  L1 MSHR
  Memory pipeline width
L2 parameters
  L2 Miss/Response Queue
  Flit Size (Crossbar)
Fully Associative Array
Moderate cost of scaling
Scale by 1.5x

## Slide 37
Cost-effective design-space
L1 parameters
  L1 Miss Queue
  L1 MSHR
  Memory pipeline width
L2 parameters
  L2 Miss/Response Queue
  Flit Size (Crossbar)
32+32 Baseline Crossbar
Scales quadratically with flit size
“Asymmetric Crossbar”

## Slide 38
Asymmetric Crossbar
Core
DRAM
L2
L1
L1-L2 Crossbar
Symmetric Crossbar
L1
L1
L2
L2
Asymmetric Crossbar
32+32 = 64
16+48 = 64
32 bytes
request
16 bytes
request
32 bytes
response
48 bytes
request
No wiring overhead
16+68 / 32+52 = 84
Wiring overhead of 20 bytes
Point-to-point
Wiring
(bytes)
Control
(8 bytes)
Cache line
(128 bytes)
Reads >> Writes

## Slide 39
Cost-effective Design Space: Summary
L1 Cache
  L1 Miss Queue : 8 entries  32 entries
  Memory pipeline width : 10 wide  40 wide
  L1 MSHR : 32 entries  48 entries
L2 Cache
  L2 Miss/Response Queue : 8 entries  32 entries
  Flit Size (Crossbar) : 32+32  16+48 (=64); 16+68/32+52 (=84)
Evaluate 3 cost-effective configurations: 16+48 16+68 32+52

## Slide 40
Results
Cost-effective configurations
23%
Area overhead: 1.1%
Point-to-point wires remains same as baseline

## Slide 41
Results
Cost-effective configurations
Area overhead: 1.6%
25%
29%
Investing in the response path gives better returns

## Slide 42
Results
Cost-effective configurations
11%
Higher speedup on resolving bandwidth bottleneck in cache hierarchy
25%
29%
Configuration with synergistic scaling (of L1 and L2) and
asymmetric crossbar with higher response bandwidth (16+68) performs best

## Slide 43
Conclusion
Problem
  High congestion across the memory hierarchy
  Congestion leads to high memory latencies (both to L2 and DRAM)
  High latencies appear in the critical path for memory-intensive applications, causing slowdown
Observation
  Characterize stalls and develop insights about bandwidth bottleneck
  Significant bandwidth bottleneck in the cache hierarchy
  Addressing bandwidth problem in isolation can even lead to slowdown
Proposal
  Synergistic scaling of bandwidth of L1 and L2 cache
  Asymmetric scaling of bandwidth of crossbar
  23% speedup with 1.1% area overhead (no additional wires in crossbar)
  29% speedup with 1.6% area overhead (additional wiring in crossbar)

## Slide 44
Questions?
Saumay Dublish
saumay.dublish@ed.ac.uk
http://homepages.inf.ed.ac.uk/s1433370/